Power Line Carrier Communication Equipment PL-9500 is a new generation equipment for carrier transmission and reception of Speech, Facsimile, RTU data, and tele-protection signals in frequency range of 32 KHz to 508 KHz over high voltage overhead transmission lines. The system offers a single channel expandable to two channels for full bandwidth Speech / Fax or Shared Speech-cum-superimposed data channel or one high-speed 4-wire exclusive data channel of 1200 bauds. The superimposed data channel can support upto 600-baud (2160-3700 Hz) channel as a backup for RTU/SCADA on wideband communication links. PL-9500 can be used either as a terminal equipment or as Drop / Insert through a coupled repeater.

### features

- Single or dual channel configurations.

- 32 KHz to 508 KHz frequency range with   1 KHz frequency allocation steps.

- 20/40W PEP power at Line output.

- On site configuration of channel frequencies and transmission levels.

- Field programmable VF upper cut off through switch selection.

- DSP based circuitry for field programmable pilot & transit band pass filters.

- Remote extension of direct EPABX lines, Hot Line, Express Channels and 2W/4W E&M modes available on same VF interface unit.

- Ease of installation and maintenance.

| SPECIFICATIONS |
| --- |
| GENARAL INFORMATION |  | GROUP DELAY |
| Multiplexing Channel Capacity Modulation VF-Band Speech Bandwidth | Analog, Frequency Division Upto 2 Channels AM, SSB Supressed carrier 300 – 3720 Hz 300 – 2000 Hz, 300 – 2200 Hz 300 – 2400 Hz, 300 – 3400 Hz |  | 500-600 Hz 600-1000 Hz 1000-2600 Hz 2600-2800 Hz | 3 mSec. (Maximum) 1.5 mSec. (Maximum) 0.5 mSec. (Maximum) 2.5 mSec. (Maximum) |
|  |  |  | SIGNALLING PILOT |
|  |  |  | Signaling Frequency Pilot Frequency Level Distortion at 10 pps, (50/50 Break / Make) AGC Range Input Output | 3825 Hz Programmable (2160, 2220 2580, 3360, & 3780 ±30Hz) -14 dBm0 <5.0 mSec (5%) -26 to +14 dB ± 1.0 dB |
| HF INTERFACE |  |  |  |
| Impedance Output Power to Line Transmission Level (40W Version) Receiver Sensitivity Return Loss Carrier Stability Carrier Leak Medium Tapping Loss (for parallel connection of an additional PLCC equipment) | 75 / 125 Ohms (Unbalanced) or 150 Ohms (balanced) 20 / 40W PEP + 38 dBm -43 dBm 12 dB minimum ± 2 ppm over the temperature range of 0( to 50( C Better than –45 dBm0 66/132/220/440 KV HVTs <1.5 dB at (f ( 8 KHz <1.5 dB at (f ( 8 KHz |  |  |  |
|  |  |  | NOISE PERFORMANCE |
|  |  |  | Idle Noise Cross Talk Side Tone (HF Terminated) Out of Band Spurious | Better than –55 dBm0p without compander Better than –65 dBm0p with compander Better than –50 dBm0p Better than –40 dBm0p Better than –60 dBm0p |
| VF INTERFACE |  |  |  |
| 2W Transmit Level 2W Receive Level 2W Impedance 2W Return Loss 4W Transmit Level 4W Receive Level 4W Impedance 4W Return Loss Frequency Response (Without Companders) 300-400 Hz 400-600 Hz 600-2400 Hz 2400-3000 Hz 3000-3400 Hz Linearity (-10 to –3.0 dBm0 input) Limiting End to End Frequency Deviation | -13.5 to +8.0dBm, 0dBm (Nom.) -17.0 to +4.5dBm, -7dBm (Nom.) 600 Ohms 14dB minimum -17.0 to 8.0dBm, -3.5dBm (Nom.) -17.0 to +8.0dBm, -3.5dBm (Nom.) 600Ohms 20dB minimum -0.9 to +3.0 dB -0.9 to +1.70 dB -0.9 to +0.9 dB -0.9 to +1.7 dB -0.9 to +3.0 dB ± 0.5 dBm0 Starts above –3 dBm0 at 2W input 2 Hz maximum |  |  |  |
|  |  |  | Power supply |
|  |  |  | Input Voltage Power Consumption (For 20W Version) (For 20W Version) | -48V Nom. (-40V to –60V) 160W (for twin channel system) 220W (for twin channel system) |
|  |  |  | MECHANICAL |
|  |  |  | Rack Size Color of Rack | Height : 1908mm Width : 690mm Depth : 500mm Swing Rack - Outside: Aircraft Grey Powder coating, Inside: Eggshell white |
|  |  |  | ENVIRONMENTAL |
|  |  |  | Meets all specs. Operational Storage Humidity | 0( C to +50( C -10( C to +55( C -25( C to +65( C 95% max. at 40( C |

Specifications subjected to change without notice. (07092012)	NOTE: Specifications hold for a pair of end to end terminals excluding coupling             equipment and HV lines impairment.

Punjab Communications Limited B-91, Phase VIII, Industrial Area, S.A.S. Nagar (Punjab) 160 071 India Phones : +91-172-2237101 (8 lines), Fax : +91-172-2237125, 3046919 e-mail : marketing@puncom.com

Visit us at our internet site : www.puncom.com

# Text boxes

Power line carrier communication – pl 9500

- Local and Remote loop-back facility.

- Can transmit trip signals from Distance Protection Scheme (Network) for the protection of high voltage transmission lines.

- Supervisory unit facilitates easy maintenance and operation.

- Extensive use of Integrated Circuits and Crystal filters ensures high quality and reliability of equipment.

- Compliance with relevant ITU-T, IEC and IS standards.

- Fully complies to the relevant EMI & EMC standards.

- Availability of Normal Rack as well as Swing Rack.

power line carrier communication – pl 9500